## Slide 1: Manufacturing’s Objectives
The goal of manufacturing is to produce
  The right goods
  Of the right quality
  In the right quantities
  At the right time
  At minimum cost

## Slide 2: Four Basic Questions
What are we going to make?
What do we need to make it?
What do we already have?
What must we procure?

## Slide 3: Priority
The APICS Dictionary defines priority as:
“the relative importance of jobs, i.e., the sequence in which jobs should be worked on.” - APICS Dictionary, 8th Edition
Priority refers to what is needed, how much is needed, and when it is needed.

## Slide 4: Capacity
The APICS Dictionary defines capacity as:
“the capability of a worker, machine, work center, plant or organization to produce output per time period.”- APICS Dictionary, 8th Edition

## Slide 5
Aggregate Production
Plan
Master Production
Schedule (MPS)
Material
Requirements
Plan (MRP)
Production Activity
Control (PAC)
Resource
Requirements
Plan (RRP)
Rough-Cut
Capacity
Plan (RCCP)
Capacity
Requirements
Plan (CRP)
Input/Output Control
Operation Sequencing
Priority Management Techniques
Capacity Management Techniques
Hierarchical Planning Process

## Slide 6: Manufacturing Planning and Control System (MPCS)
Strategic Business Plan - A statement of the major goals and objectives the company expects to achieve over the next 2-10 years or more.
  - broad/general direction
  - low level of detail
  - long-range forecasts
  - responsibility of senior management
  - includes Marketing, Finance, & Production participation
  - usually reviewed every six months to a year

## Slide 7: MPCS
Aggregate Production Plan (APP) must
  Satisfy market demand within resources available
  Assist strategic business plan implementation
  Based upon families of products
  Fairly low level of detail
  Address a six to 18 month planning horizon
  Reviewed each month or quarter

## Slide 8: MPCS
Master Production Schedule - Plan for the production of individual end items (finished goods).
  breaks down aggregate production plan
  list the quantity of each end item to be made
  level of detail is higher than the aggregate production plan
  developed for individual end items
  three to 18 month planning horizon
  reviewed and changed weekly or monthly

## Slide 9: MPCS
Material Requirements Plan (MRP) - Plan for the production and purchase of the components used in making the items in the MPS
  Production control & purchasing use MRP to decide the purchase or manufacture of specific items
  Level of detail is high
  Determines when the components & parts are needed
  Planning horizon is at least as long as the combined purchase and manufacture lead times (3 to 18 months)
  Usually reviewed daily or weekly

## Slide 10: MPCS
Production Activity Control & Purchasing
  Represents the implementation & control phase
  Purchasing is responsible for establishing and controlling flow of raw materials into the factory
  PAC is responsible for planning & controlling flow of work through the factory
  Planning horizon is very short, a day to a month
  Level of detail is high
  Reviewed and revised daily

## Slide 11: MPCS
At each level in the MPCS, 3 questions must be
answered:
  1. What are the priorities - how much of what is
  to be produced & when?
  2. What is the available capacity - what resources do
  we have?
  3. How can differences between priorities &
  capacity be resolved?

## Slide 12: Manufacturing Resource Planning (MRP II)
Manufacturing resource planning (MRP II) is a method for the effective planning of all resources of a manufacturing company. Ideally, it addresses operational planning in units, financial planning in dollars, & has a simulation capability to answer “what if” questions.
It is made up of a variety of functions, each linked together: business planning, sales and operations planning, production planning, master production scheduling, material requirements planning, capacity requirements planning, and the execution support systems for capacity & material.
Output from these systems is integrated with financial reports such as the business plan, purchase commitment report, shipping budget, & inventory projections in dollars.
- APICS Dictionary, 8th edition, 1995

## Slide 13: Creating the APP
APP is
  . . . setting the overall level of manufacturing output . . . & other activities to best satisfy the current planned levels of sales . . . while meeting general business objectives of profitability, productivity . . . etc., as expressed in the overall business plan.
  - APICS Dictionary, 8th edition, 1995

## Slide 14: Creating the APP
APP is concerned with
  Quantities of each product group in each period.
  Desired inventory levels.
  Resources of equipment, labor, & material needed
  Availability of needed resources
Why are plans made for product groups?
What should the product groups be based on?

## Slide 15: Creating the APP
APP characteristics
  Time horizon may be more or less than 12 months, depending on the manufacturing cycle
  Demand is seasonal for many products, but not for all (seasonal demand is the worst-case scenario)
  Plan is made for families or groups
  Management will have a variety of objectives
What might be some management objectives?

## Slide 16: Developing the APP
Three Basic Strategies
  Chase (Demand Matching) Strategy: Produce the amounts that are demanded at any one time
  Production Leveling Strategy: Continuously produce an amount equal to the average demand
  Subcontracting: Meeting additional demand through subcontracting
Hybrid Strategy: Combination of any of the above strategies

## Slide 17: Chase APP Strategy
Chase (demand matching) Strategy
  - Produce the amounts demanded at any given time.
  - Inventory levels remain stable as production varies
  to meet demand.
Units
1 2 3 4 5 6 7 8 9 10 11 12
Periods

## Slide 18: Chase APP Strategy
• Chase Strategy Disadvantages
  As production increases, workers must be hired and trained - increases cost.
  As production decreases, people are laid off and morale suffers - increases cost
  When production starts to increase again, the best workers may have other jobs and their skills will not be available
  Manufacturing must have enough plant capacity to produce at the highest capacity needed
• What industries use a chase strategy?

## Slide 19: Level APP Strategy
• Production Leveling Strategy
  - Continuously produce an amount equal to the average demand
  - Maintain stable workforce
1 2 3 4 5 6 7 8 9 10 11 12
Units
Periods

## Slide 20: Level APP Strategy
Production Leveling Strategy
  Avoids the disadvantages of demand matching
  However, inventory builds up
What are some examples of industries that could use this strategy?

## Slide 21: Subcontracting & APP
• Subcontracting Strategy
  Producing at the level of minimum demand & meeting additional demand through subcontracting
• Major Advantage
  Excess capacity costs are avoided
  Since production is leveled, there are no costs associated with changing production levels
• Major Disadvantages
  Purchasing cost may be greater than if made in-house Certain core skills or technologies may be lost

## Slide 22: Hybrid APP Strategy
  • Hybrid Strategy
  - Combination of any of the 3 strategies
  - Combination of strategies that
  • minimizes the sum of all costs involved
  • provides required level of service
  • meets financial & marketing plan objectives

## Slide 23: APP Using Pure Strategies
Hiring cost = $100 per worker Firing cost = $500 per worker
Inventory carrying cost = $0.50 pound per quarter
Production per employee = 1,000 pounds per quarter
Beginning work force = 100 workers
Quarter Sales Forecast (lb)
Spring 80,000
Summer 50,000
Fall 120,000
Winter 150,000

## Slide 24: Level Production Strategy
Sales Production
Quarter Forecast Plan Inventory
Spring 80,000 100,000 20,000
Summer 50,000 100,000 70,000
Fall 120,000 100,000 50,000
Winter 150,000 100,000 0
400,000 140,000
Cost = 140,000 pounds x 0.50 per pound = $70,000

## Slide 25: Chase Demand Strategy
Sales Production Workers Workers Workers
Quarter Forecast Plan Needed Hired Fired
Spring 80,000 80,000 80 - 20
Summer 50,000 50,000 50 - 30
Fall 120,000 120,000 120 70 -
Winter 150,000 150,000 150 30 -
100 50
Cost = (100 workers hired x $100) + (50 workers fired x $500)
= $10,000 + 25,000 = $35,000

## Slide 26: Strategies for Managing Demand
Shift demand into other periods
  incentives, sales promotions, advertising campaigns
Offer product or services with countercyclical demand patterns
  create demand for idle resources

## Slide 27: Hierarchical Planning Process
Items
Product lines or families
Individual products
Components
Manufacturing operations
Resource level
Plants
Individual machines
Critical work centers
Production Planning
Capacity Planning
Resource
Requirements Plan
Rough-Cut
Capacity Plan
Capacity
Requirements Plan
Input/Output
Control
Aggregate
Production Plan
Master Production
Schedule
Material
Requirements Plan
Shop Floor
Schedule
All work centers