## Slide 1: Master Production Scheduling (MPS)
MPS states the requirements for individual end items by date & quantity
Limited by the APP & must “disaggregate” the APP
Master planning seeks to plan & control the impact of independent demand on material & capacity

## Slide 2: Master Production Scheduling (MPS)
MPS is a vital link between sales & production
  Makes possible valid order promises
  Represents a contract between sales and production.

## Slide 3: MPS Inputs
Inputs to the MPS include
  Forecast
  APP
  Orders from customers &/or additional independent demand
  Inventory levels
  Capacity constraints

## Slide 4: MPS Objectives
The objectives of the MPS are to
  Maintain the desired level of customer service
  Make the best use of resources
  Keep inventories at the desired level

## Slide 5: MPS Objectives & Preparation
MPS objectives
  Maintain the desired level of customer service
  Make the best use of resources
  Keep inventories at the desired level
Make a preliminary MPS - disaggregate the APP
Perform rough-cut capacity planning
Resolve differences

## Slide 6: Rough-cut Capacity Planning
Rough-cut capacity planning checks whether critical resources are available to support the preliminary master schedule
A resource bill shows the time required for individual items on a critical resource
What are some possible critical resources?

## Slide 7: Resolving Differences
Available capacity must be equal to or greater than required capacity
If required capacity exceeds available capacity
  Capacity must be increased
  or
  Plan must be altered
How can capacity be increased or demand be decreased?

## Slide 8: Resolving Differences
The MPS must be judged by three criteria
  Resources use. Is the MPS within capacity restraints in each period of the plan? Does it make the best use of resources?
  Customer service. Will due dates be met and will delivery performances be acceptable?
  Cost. Is the plan economical, or will excess cost be incurred for overtime, subcontracting, expediting, or transportation?

## Slide 9: MPS & Sales
MPS is not a sales forecast, it is instead a forecast of production.
It may not necessarily be what we want; it should be what we can do.
MPS must be realistic & achievable; otherwise, the plan fails, deliveries are not met, & manufacturing has to react to circumstances rather than planning for them

## Slide 10: MPS and Delivery Promises
As orders are received, they “consume” available production and inventory
Any part not consumed is available-to-promise
Customer
Orders
Available-to-
Promise
Time
Units
Production Capacity or Inventory

## Slide 11: Available-to-Promise
Available-to-Promise is
  the uncommitted portion of a company’s inventory & planned production
  maintained in the master schedule to support customer order promising
  the uncommitted inventory balance in the first period & is normally calculated for each period in which an MPS receipt is scheduled
  APICS Dictionary, 8th edition

## Slide 12: Available-to-Promise
ATP calculation assumes that the entire ATP will be sold before the next scheduled receipt
When calculating ATP, consider all orders until the next scheduled receipt, e.g.,
ATP for period 1
= on hand - customer orders due b4 next MPS scheduled receipt
ATP for periods 2, 4, and 6
= MPS scheduled receipt - customer orders due b4 next MPS scheduled receipt

## Slide 13: Available-to-Promise
Period
1
2
3
4
5
6
Customer Orders
160
20
20
50
MPS Scheduled
Receipts
200
200
200
Available
to
Promise
40
On hand = 200 units

## Slide 14: Available-to-Promise
On hand = 200 units

## Slide 15: Available-to-Promise
On hand = 200 units

## Slide 16: Planning Horizon
The planning horizon is defined as
“the amount of time the master schedule extends into the future. This is normally set to cover a minimum of cumulative lead time plus time for lot sizing low-level components and for capacity changes of primary work centers or of key suppliers.”
  APICS Dictionary, 8th edition

## Slide 17: Planning Horizon
What is the minimum planning
horizon in this example?
B
A
C
D
E
Lead Time
= 6 weeks
Lead Time
= 2 weeks
Lead Time
= 5 weeks
Lead Time
= 8 weeks
Lead Time
= 16 weeks

## Slide 18: Time Fences and Zones
0
Actual Orders
(Emergency
Changes Only)
Frozen
Slushy
Liquid
Actual and Forecast
(Trade-offs)
Forecast Only
(Changes constrained by production plan)
Due
Date
Demand
Time
Fence
Planning
Time
Fence
2 weeks
26 weeks

## Slide 19: Summary
MPS Major Functions
  Forms the link between APP & what manufacturing builds
  Plans capacity requirements - the MPS determines the capacity required
  Plans material requirements - the MPS drives the (MRP)
  Keeps priorities valid - the MPS is a priority plan for manufacturing

## Slide 20: Summary
MPS Links Sales & Production
  Aids in making order promises - the MPS is a plan for what is to be produced & when
  Informs sales & manufacturing when goods will be available for delivery
  Creates a contract between marketing & manufacturing - an agreed-upon plan

## Slide 21: Summary
The MPS must be realistic & based on what production can & will do, if not,
  Resource overloads or underloads occur
  Unreliable schedules result & delivery performance suffers
  High levels of work-in-process (WIP) inventory build-up
  Customer service is poor
  Planning system loses credibility