## Slide 1: Capacity Management
Capacity management is planning & controlling resources needed to meet production objectives
  Planning: determining resources needed to meet the priority plan; selecting methods to make that capacity available
  Controlling: monitoring output, comparing it with the plan, & taking corrective action

## Slide 2: Matching Capacity and Demand
Demand Management
  vary prices
  change lead times
  encourage/discourage business
Capacity Management
  adjust staffing
  adjust equipment and processes
  change methods to facilitate production
  redesign the product to facilitate production

## Slide 3: Capacity Planning Process
Determine the capacity available @ each work center
Translate the released & planned orders into the capacity required @ each work center in each time period
Sum up the capacities required for each work center to determine the load on each work center in each time period
Resolve differences between available capacity and required capacity

## Slide 4: Resource Planning
RP involves long-range capacity resource requirements & directly linked to production planning
RP involves changes in manpower, capital equipment, product design, or other facilities that take a long time to acquire & eliminate.
The production plan & RP set the limits and levels for production

## Slide 5: Rough-Cut Capacity Planning
RCCP is the process to
  check feasibility of the MPS (end items)
  provide warnings of any bottlenecks
  ensure utilization of work centers
  advise vendors of capacity requirements

## Slide 6: Capacity Requirements Planning (CRP)
CRP is directly linked to the MRP (component items)
CRP is the most detailed, complete, & accurate of the capacity planning techniques & is highly important in the immediate time periods

## Slide 7: Inputs for Capacity Planning
Inputs needed are:
  open shop orders from open order file
  planned order releases from MRP
  routings and time standards from the routing file
  lead times and work center capacities from the work center file

## Slide 8: Inputs for Capacity Planning
Planned order releases are determined by the computer’s MRP logic based upon the gross requirements for a particular part. Used to help assess the total capacity required in future time periods.

## Slide 9: Inputs for Capacity Planning
Routing file is the path that work follows from work center to work center as it is completed and should contain:
  Operations to be performed
  Sequence of operations
  Work centers to be used
  Possible alternate work centers
  Tooling needed for each operation
  Standard times: setup times and run times per piece

## Slide 10: Inputs for Capacity Planning
Work center file is composed of a number of machines or workers capable of doing the same work and should contain
  Move time -- time taken to move material from one workstation to another
  Wait time -- time a job is at a work center after completion & before being moved
  Queue time -- time a job waits at a work center before being handled
  Lead time -- sum of queue, setup, run, wait, & move times

## Slide 11: Determining Capacity Available
To calculate available capacity, we need:
Available time = # of machines*# of workers*# hours of operation
Utilization = % of time that the work center is actually active
Efficiency = a ratio of the actual output to standard expected output

## Slide 12: Utilization and Efficiency Problem
A work center produces 90 standard hours of work in one week. The hours available are 80, and 70 are actually worked. Calculate the utilization and efficiency of the work center.

## Slide 13: Rated Capacity
Rated capacity = measure of the output that can be expected for a work center
Rated Capacity = available time x utilization x efficiency
e.g.,
A work center has 3 machines and is operated 8 hours a day for 5 days/week. Past utilization has been 75% & efficiency has been 110%. What is the rated capacity?
Available time = 3 x 8 x 5 = 120 hours per week
Rated capacity = 120 x 0.75 x 1.10 = 99 standard hours

## Slide 14: Demonstrated (Measured) Capacity
Demonstrated capacity = proven capacity calculated from actual performance data (i.e., average capacity)
e.g.,
Over the previous four weeks, a work center produced 110, 140, 120, & 130 standard hours of work. What is the demonstrated capacity?

## Slide 15: Required Capacity
Determining required capacity:
(1)determine time needed for each order at each work center = sum setup time & run time (i.e., standard operating time-SOT)
(2) sum capacity required for individual orders to obtain a load
 | Order Qty | Setup Time | Run Time | SOT
Released Orders |  |  |  | 
100 | 100 | 0.0 | 0.2 | 20.0 Std. Hrs.
200 | 150 | 1.5 | 0.2 | 31.5 Std. Hrs.
Planned Orders |  |  |  | 
400 | 200 | 3.0 | 0.25 | 53.0 Std. Hrs.
500 | 300 | 2.5 | 0.15 | 47.5 Std. Hrs.
Total Time |  |  |  | 152.0 Std. Hrs.

## Slide 16: Scheduling Orders
Calculate SOT @ each work center
  SOT=setup time + (run time per piece x number of pieces)
Calculate lead time
  Lead time = SOT + queue time + wait time + move time
Back Scheduling - start with the due date and, using the lead times, to work back to find the start date for each operation

## Slide 17: Resolving Differences
Change Capacity
    Overtime or undertime - Hiring or layoff
    Shift work force - Alternate routings
    Subcontract
Alter Load
    Alter lot sizes - Reschedule