## Slide 1: Statistical Process Control
Take periodic samples from a process
Plot the sample points on a control chart
Determine if the process is within limits
Correct the process before defects occur

## Slide 2: Types Of Data
Attribute data
    Product characteristic evaluated with a discrete choice
      Good/bad, yes/no
Variable data
    Product characteristic that can be measured
      Length, size, weight, height, time, velocity
Notes: Attribute data describe product or service characteristics that can be counted or classified, such as number of defective items, number of customer complaints, or percent of students who passed a test.
Variable data describe product or service characteristics that can be measured, such as weight, length, or time.

## Slide 3: SPC Applied To Services
Nature of defect is different in services
Service defect is a failure to meet customer requirements
Monitor times, customer satisfaction

## Slide 4: Service Quality Examples
Hospitals
  timeliness, responsiveness, accuracy
Grocery Stores
  Check-out time, stocking, cleanliness
Airlines
  luggage handling, waiting times, courtesy
Fast food restaurants
  waiting times, food quality, cleanliness

## Slide 5: Run Charts & Control Charts
Run Charts
  Run charts are used to detect trends or patterns
  Same model as scatter plots
Control Charts
  Run charts turn into control charts
  One of the single most effective quality control devices for managers and employees

## Slide 6: Control Chart
Periodic tracking of a process
Common types
  Xbar, R or range, p or percent nonconforming
Elements of a control chart
  upper control limit (UCL), the highest value a process should produce
  central line (Xbar), the average value of consecutive samples
  lower control limit (LCL), the lowest value a process should produce

## Slide 7: Control Charts - Xbar
Shows average outputs of a process
UCL
LCL
Central line- Xbar
Scale

## Slide 8: Control Charts - R
Shows the uniformity/dispersion of the process
UCL
LCL
Central line- Rbar
Scale

## Slide 9: Constructing a Control Chart
Decide what to measure or count
Collect the sample data
Plot the samples on a control chart
Calculate and plot the control limits on the control chart
Determine if the data is in-control
If non-random variation is present, discard the data (fix the problem) and recalculate the control limits

## Slide 10: A Process Is In Control If
No sample points are outside control limits
Most points are near the process average
About an equal # points are above & below the centerline
Points appear randomly distributed

## Slide 11: The Normal Distribution
m = 0
1s
2s
3s
-1s
-2s
-3s
99.74 %
95 %
Area under the curve = 1.0
Notes: Figure 4.2

## Slide 12: Control Chart Z Values
Smaller Z values make more sensitive charts
Z = 3.00 is standard
Compromise between sensitivity and errors

## Slide 13: Control Charts and the Normal Distribution
Mean
UCL
LCL
+ 3 s
- 3 s
.

## Slide 14: Types Of Data
Attribute data (p-charts, c-charts)
    Product characteristics evaluated with a discrete choice (Good/bad, yes/no, count)
Variable data (X-bar and R charts)
    Product characteristics that can be measured (Length, size, weight, height, time, velocity)
Notes: Control charts exist for attributes and variables. Within each category there are several different types of control charts. We will discuss mean and range charts for variables, and p-charts and c-charts for attributes.
Variable data describe product or service characteristics that can be measured, such as weight, length, or time. Attribute data describe product or service characteristics that can be counted or classified, such as number of defective items, number of customer complaints, or percent of students who passed a test.

## Slide 15: Control Charts For Attributes
p Charts
  Calculate percent defectives in a sample;
  An item is either good or bad
c Charts
  Count number of defects in an item
Notes: A p-chart measures the number of defectives as a percentage of the total number of possible defectives.
A c-chart measures the actual number of defectives in a sample when the total number of possible defectives is not known. For example, the number of blemishes in a paint job, the number of bubbles in a sheet of glass, or the number of picks in a bolt of cloth would be graphed on a c-chart.

## Slide 16: p - Charts
Based on the binomial distribution
  p = number defective / sample size, n
  p = total no. of defectives
    total no. of sample observations
  UCLp = p + 3 p(1-p)/n LCLp = p - 3 p(1-p)/n
DSCI 3123

## Slide 17
c - Charts
Count the number of defects in an item
Based on the Poisson distribution
  c = number of defects in an item
  c = total number of defects
  number of samples
  UCLc = c + 3 c LCLc = c - 3 c
DSCI 3123

## Slide 18: Control Charts For Variables
Mean chart (X-Bar Chart)
  Measures central tendency of a sample
Range chart (R-Chart)
  Measures amount of dispersion in a sample
Each chart measures the process differently. Both the process average and process variability must be in control for the process to be in control.
Notes: The mean or X-bar chart indicates how sample results relate to the process average or mean. The range or R chart reflects the amount of dispersion that is present in each sample. These charts are normally used together to determine if a process is in control.

## Slide 19: Example: Control Charts for Variable Data
Slip Ring Diameter (cm)
Sample 1 2 3 4 5 X R
1 5.02 5.01 4.94 4.99 4.96 4.98 0.08
2 5.01 5.03 5.07 4.95 4.96 5.00 0.12
3 4.99 5.00 4.93 4.92 4.99 4.97 0.08
4 5.03 4.91 5.01 4.98 4.89 4.96 0.14
5 4.95 4.92 5.03 5.05 5.01 4.99 0.13
6 4.97 5.06 5.06 4.96 5.03 5.01 0.10
7 5.05 5.01 5.10 4.96 4.99 5.02 0.14
8 5.09 5.10 5.00 4.99 5.08 5.05 0.11
9 5.14 5.10 4.99 5.08 5.09 5.08 0.15
10 5.01 4.98 5.08 5.07 4.99 5.03 0.10
50.09 1.15
Notes: Example4.3

## Slide 20: Constructing an Range Chart
UCLR = D4 R = (2.11) (.115) = 2.43
LCLR = D3 R = (0) (.115) = 0
where R = S R / k = 1.15 / 10 = 0.115
k = number of samples = 10
R = range = (largest - smallest)

## Slide 21: 3s Control Chart Factors
Sample size X-chart R-chart
n A2 D3 D4
2 1.88 0 3.27
3 1.02 0 2.57
4 0.73 0 2.28
5 0.58 0 2.11
6 0.48 0 2.00
7 0.42 0.08 1.92
8 0.37 0.14 1.86
Notes: Table 4.1

## Slide 22: Constructing A Mean Chart
UCLX = X + A2 R = 5.01 + (0.58) (.115) = 5.08
LCLX = X - A2 R = 5.01 - (0.58) (.115) = 4.94
where X = average of sample means = S X / n
= 50.09 / 10 = 5.01
R = average range = S R / k = 1.15 / 10 = .115

## Slide 23: Variation
Common Causes
  Variation inherent in a process
  Can be eliminated only through improvements in the system
Special Causes
  Variation due to identifiable factors
  Can be modified through operator or management action

## Slide 24: Control Chart Patterns
UCL
LCL
LCL
UCL
Sample observations
consistently below the
center line
Sample observations
consistently above the
center line

## Slide 25: Control Chart Patterns
LCL
LCL
UCL
UCL
Sample observations
consistently increasing
Sample observations
consistently decreasing

## Slide 26: Control Chart Patterns
UCL
LCL
LCL
UCL
Sample observations
consistently below the
center line
Sample observations
consistently above the
center line

## Slide 27: Control Chart Patterns
1. 8 consecutive points on one side of the
center line
2. 8 consecutive points up or down
across zones
3. 14 points alternating up or down
4. 2 out of 3 consecutive points in Zone A
but still inside the control limits
5. 4 out of 5 consecutive points in Zone A or B

## Slide 28: Zones For Pattern Tests
UCL
LCL
Zone A
Zone B
Zone C
Zone C
Zone B
Zone A
x + 2 sigma
x + 1 sigma
x + 3 sigma
x - 1 sigma
x - 2 sigma
x - 3 sigma
X
5.08
5.05
5.03
5.01
4.98
4.965
4.94
Notes: Figure 4.4