## Slide 1: Facility Layout
Objectives of Facility Layout
Basic Types
  Service Process Layout
  Product Layout
  Product vs. Process Layouts
Designing Process Layouts
Designing Product Layouts
Product Layouts & Line Balancing

## Slide 2: Objectives of Facility Layout
Minimize material handling costs
Utilize space and labor efficiently
Eliminate bottlenecks
Facilitate communication
Reduce manuf. cycle time or customer service time
Promote product and service quality
& Many others

## Slide 3: Basic Types of Layouts
Process Layout
  machines grouped by process they perform
Product Layout
  linear arrangement of workstations to produce a specific product
Fixed Position Layout
  used in projects where the product cannot be moved

## Slide 4: Hybrid Layouts
Cellular layouts
  group machines into machining cells
Flexible manufacturing systems
  automated machining & material handling systems
Mixed-model assembly lines
  produce variety of models on one line

## Slide 5: Manufacturing Process Layout
L
L
L
L
L
L
L
L
L
L
M
M
M
M
D
D
D
D
D
D
D
D
G
G
G
G
G
G
P
P
A
A
A
Assembly
Painting Department
Lathe Department
Milling Department
Drilling Department
Grinding Department
Receiving and
Shipping

## Slide 6: Service Process Layout
Women’s
dresses
Women’s
sportswear
Shoes
Cosmetics
& Jewelry
Entry &
display area
Housewares
Men’s
department
Children’s
department
Power Tools

## Slide 7: A Product Layout
IN
OUT

## Slide 8: Product vs. Process Layouts
PRODUCT LAYOUT PROCESS LAYOUT
1. Description Sequential arrangement Functional grouping
of machines of machines/areas
2. Type of Continuous, mass Intermittent, job shop,
Process production, assembly batch production
3. Product Standardized, make-to-stock Varied, make-to-order
4. Storage Small Large
(IKEA?)

## Slide 9: Designing Process Layouts
Minimize material handling costs
Block Diagramming
  minimize nonadjacent loads
  use when quantitative data is available
Relationship Diagramming
  based on location preference between areas
  use when quantitative data is not available

## Slide 10: Block Diagramming
Examples in Chapter 8 – pg 168-172
Create load summary chart
Calculate composite (2-way) movements (if necessary)
Develop trial layouts minimizing number of nonadjacent loads (i.e., this means min cost or distance)
Assume nonadjacent loads are 2x (expense or distance)

## Slide 11
LOAD SUMMARY CHART($)
DEPARTMENT
DEPT.
1
2
3
4
5
1
100
110
2
200
150
3
40
50
4
5
50
60

## Slide 12: Initial & Final Designs

## Slide 13: Relationship Diagramming
Used when quantitative data is not available
Muther’s grid displays preferences
Denote location preferences with weighted lines

## Slide 14: Ranking System For Departments
A - absolutely necessary
E - especially important
I - important
O - okay
U - unimportant
X - undesirable

## Slide 15: Relationship Diagramming Example
Production
Offices
Stockroom
Shipping and Receiving
Locker Room
Toolroom
A
A
A
O
O
O
O
O
U
U
U
U
E
X
I

## Slide 16: Service Layouts
Usually process layouts
Minimize flow of customers or paperwork
Retailing tries to maximize customer exposure to products
Computer programs consider shelf space, demand, profitability
Layouts must be aesthetically pleasing

## Slide 17: Designing Product Layouts (assembly lines)
Precedence diagram
  network showing order of tasks and restrictions on their performance
Cycle time
  maximum time product can spend at any one workstation; largest workstation time; how often a product is completed
Example in Chapter 8 – pg 175-177

## Slide 18: Product Layouts & Line Balancing
1. Draw and label a precedence diagram
2. Calculate desired cycle time
3. Calculate theoretical min # of workstations
4. Group elements into the minimum # of workstations recognizing cycle time and precedence constraints
5. Calculate efficiency of the line
6. Stop if desired efficiency or # workstations; else go to step 4

## Slide 19: Drawing A Precedence Diagram
Work element Precedence time
Press out sheet of fruit - 0.1
Cut into strips A 0.2
Outline fun shapes A 0.4
Roll up and package B, C 0.3
C
D
B
A
0.1
0.2
0.4
0.3

## Slide 20: Computing Cycle Time
Maximum time product can spend at any station
What cycle time do we need to produce
6,000 units in a 40 hour week?
production time available
desired output
C =
40 x 60
6,000
C =
= 0.4

## Slide 21: Flow Time vs. Cycle Time
Flow time = time to complete all stations
Cycle time = max time spent at any station
Flow time = 0.1 + 0.2 + 0.4 + 0.3
= 1.0
Cycle time = max (0.1, 0.2, 0.4,0.3) = 0.4
C
D
B
A
0.1
0.2
0.4
0.3
0.1, 0.2
0.4
0.3

## Slide 22: Balancing The Line - Straight Line
Workstation Task Remaining time Feasible tasks
1 A 0.3 B
B 0.1 none
2 C 0.0 none
3 D 0.1
1
2
3
0.3 min
0.4 min
0.3 min
A, B
C
D

## Slide 23: Calculating Efficiency