## Slide 1: Inputs and Outputs to Aggregate Production Planning
Aggregate
Production
Planning
Company
Policies
Financial
Constraints
Strategic
Objectives
Units or dollars
subcontracted,
backordered, or
lost
Capacity
Constraints
Size of
Workforce
Production
per month
(in units or $)
Inventory
Levels
Demand
Forecasts

## Slide 2: Scheduling
Specifies when
  labor
  equipment
  facilities
  are needed to produce a product or provide a
  service
  Last stage of planning before production occurs

## Slide 3: Scheduling Function By Process Type
Process Industry
  linear programming
  EOQ with noninstantaneous replenishment
Mass Production
  assembly line balancing
Project
  project -scheduling techniques (PERT, CPM)

## Slide 4: Scheduling Batch/Job Shop Operations
Batch Production
  many planning steps
    aggregate planning
    master scheduling
    material requirements planning (MRP)
    capacity requirements planning (CRP)
Scheduling determines
  machine/worker/job assignments
  resource/requirement matchings

## Slide 5: Difficulties Of Job Shop Scheduling
Variety of jobs (customers) processed
Distinctive routing and processing requirements of each job/customer
Number of different orders in the facility at any one time
Competition for common resources

## Slide 6: This Variety Necessitates
Planning for the production of each job as it arrives
Scheduling its use of limited resources
Monitoring its progress through the system

## Slide 7: Objectives in Scheduling
Meet customer due dates
Minimize job lateness
Minimize response time
Minimize completion time
Minimize time in the system
Minimize overtime
Maximize machine or labor utilization
Minimize work-in-process inventory

## Slide 8: Responsibilities of Production Control Department
1. Loading - Check availability of material, machines & labor
2. Sequencing - Release work orders to shop & issue dispatch lists for individual machines
3. Monitoring - Maintain progress reports on each job until it is complete

## Slide 9: Loading
Allocate work to machines (resources)
Perform work on most efficient resources
Use assignment method of linear programming to determine allocation

## Slide 10: Sequencing
Prioritize jobs assigned to a resource
If no order specified use first-come first-served (FCFS)
Many other sequencing rules exist
Each attempts to achieve to an objective

## Slide 11: Sequencing Rules
FCFS - first-come, first-served
LCFS - last come, first served
SPT - shortest processing time
DDATE - earliest due date
SLACK - smallest slack
  (due date - today’s date) - (remaining processing time)
RWK - remaining work on all operations

## Slide 12: Guidelines for Selecting a Sequencing Rule
1. SPT most useful when shop is highly congested
2. Use SLACK or S/OPN for periods of normal activity
3. Use DDATE when only small tardiness values can be tolerated
4. Use LPT if subcontracting is anticipated
5. Use FCFS when operating at low-capacity levels
6. Do not use SPT to sequence jobs that have to be assembled with other jobs at a later date

## Slide 13: Monitoring
Gantt Chart
  shows both planned and completed activities against a time scale
Input / Output Control
  monitors the input and output from each work center

## Slide 14: Gantt Chart
1
2
3
4
5
6
8
9
10
11
12
1
2
3
Days
Job 32B
Job 23C
Job 11C
Job 12A
Facility
Key:
Planned
Activity
Completed
Activity
Behind schedule
Ahead of schedule
On schedule

## Slide 15: Gantt Chart Solution

## Slide 16: Employee Scheduling
Labor is very flexible resource
Scheduling workforce is complicated repetitive task
Assignment method can be used
Heuristics are commonly used
LP is also commonly used

## Slide 17: Sequencing Jobs Through Two Serial Process
1. List time required to process each job at each machine. Set up a one-dimensional matrix to represent desired sequence with # of slots equal to # of jobs.
2. Select smallest processing time at either machine. If that time is on machine 1, put the job as near to beginning of sequence as possible.
3. If smallest time occurs on machine 2, put the job as near to the end of the sequence as possible.
4. Remove job from list.
5. Repeat steps 2-4 until all slots in matrix are filled & all jobs are sequenced.

## Slide 18: Johnson’s Rule Example
A 6 8
B 11 6
C 7 3
D 9 7
E 5 10
Machine Machine
Job Center 1 Center 2
E A D B C

## Slide 19: Sequencing Jobs Through Many Machines / Processes
Facility is dynamic, new jobs added
Develop global sequencing rules
  first-in-system, first-served (FISFS)
  work-in-next-queue (WINQ)
  fewest # remaining operations (NOPN)
  slack per remaining operation (S/OPN)
  remaining work (RWK)
Study system via simulation