## Slide 1: Inputs and Outputs to Aggregate Production Planning
Aggregate
Production
Planning
Company
Policies
Financial
Constraints
Strategic
Objectives
Units or dollars
subcontracted,
backordered, or
lost
Capacity
Constraints
Size of
Workforce
Production
per month
(in units or $)
Inventory
Levels
Demand
Forecasts

## Slide 2: Scheduling
Specifies when
  labor
  equipment
  facilities
  are needed to produce a product or provide a
  service
  Last stage of planning before production occurs

## Slide 3: Difficulties Of Scheduling
Variety of jobs (customers) processed
Distinctive routing and processing requirements of each job/customer
Number of different orders in the facility at any one time
Competition for common resources

## Slide 4: This Variety Necessitates
Planning for the production of each job as it arrives
Scheduling its use of limited resources
Monitoring its progress through the system

## Slide 5: Objectives in Scheduling
Meet customer due dates
Minimize job lateness
Minimize response time
Minimize completion time
Minimize time in the system
Minimize overtime
Maximize machine or labor utilization
Minimize work-in-process inventory

## Slide 6: What is JIT ?
Producing only what is needed when it is needed
A philosophy
An integrated management system.
JIT’s mandate: Eliminate all waste.

## Slide 7: Total Cost at Q*

## Slide 8: Basic Elements of JIT
1. Flexible resources
2. Cellular layouts
3. Pull production system
4. Kanban production control
5. Small-lot production w/Quick setups
6. Uniform production
7. Quality at the source
8. Total productive maintenance
9. Supplier networks

## Slide 9: Examples of Waste
Watching a machine run or waiting for parts
Counting parts
Overproduction
Moving parts over long distances
Storing inventory
Looking for tools
Machine breakdown
Rework

## Slide 10: Flexible Resources
Multifunctional workers
General purpose machines
Study operators & improve operations

## Slide 11: Kanban Production Control System
A kanban is a card that indicates a standard quantity of production
Kanbans maintain the discipline of pull production
  - A production kanban authorizes production
  - A withdrawal kanban authorizes the movement of goods

## Slide 12: A Sample Kanban
Machining
M-2
Assembly
A-4
Part no.: 7412
Description: Slip rings
From :
To:
Box capacity 25
Box Type A
Issue No. 3/5

## Slide 13: The Origin Of Kanban
Q = order quantity
R = reorder point
= demand during lead time
Bin 1
Bin 2
Q - R
R
Reorder
Card
Kanban
a. Two-bin inventory system b. Kanban Inventory System

## Slide 14: Kanban Squares
X
X
X
X
X
X
Flow of work
Flow of information

## Slide 15: Types Of Kanbans
Kanban Square
  marks area designed to hold items
Signal Kanban
  triangular kanban signals production at the previous workstation
Material Kanban
  orders material in advance of a process
Supplier Kanban
  rotates between the factory and supplier

## Slide 16: Small-Lot Production
Requires less space & capital investment
Moves processes closer together
Makes quality problems easier to detect
Makes processes more dependent on each other

## Slide 17: Inventory Hides Problems
Poor
Quality
Unreliable
Supplier
Machine
Breakdown
Inefficient
Layout
Bad
Design
Lengthy
Setups

## Slide 18: Lower Levels Of Inventory To Expose Problems
Poor
Quality
Unreliable
Supplier
Machine
Breakdown
Inefficient
Layout
Bad
Design
Lengthy
Setups

## Slide 19: Uniform Production
Results from smoothing production requirements
Kanban systems can handle +/- 10% demand changes
Smooths demand across the planning horizon
Mixed-model assembly steadies component production

## Slide 20: Quality At The Source
Jidoka is the authority to stop a production line
Andon lights signal quality problems
Undercapacity scheduling allows for planning, problem solving & maintenance
Visual control makes problems visible
Poka-yoke prevents defects

## Slide 21: Kaizen
Continuous improvement
Requires total employment involvement
The essence of JIT is the willingness of workers to
    spot quality problems,
    halt production when necessary,
    generate ideas for improvement,
    analyze problems, and
    perform different functions

## Slide 22: Trends In Supplier Policies
1. Locate near to the customer
2. Use small, side loaded trucks and ship mixed loads
3. Consider establishing small warehouses near to the customer or consolidating warehouses with other suppliers
4. Use standardized containers and make deliveries according to a precise delivery schedule
5. Become a certified supplier and accept payment at regular intervals rather than upon delivery

## Slide 23: Benefits Of JIT
1. Reduced inventory
2. Improved quality
3. Lower costs
4. Reduced space
requirements
5. Shorter lead time
6. Increased productivity
7. Greater flexibility
8. Better relations with suppliers
9. Simplified scheduling and control activities
10. Increased capacity
11. Better use of human
resources
12. More product variety

## Slide 24: JIT Implementation
Use JIT to finely tune an operating system
Somewhat different in USA than Japan
JIT is still evolving
JIT isn’t for everyone

## Slide 25: JIT In Services
Competition on speed & quality
Multifunctional department store workers
Work cells at fast-food restaurants
Just-in-time publishing for textbooks
Construction firms receiving material just as needed (Empire State Building - classic example)